## Slide 1: Objective
Employ deterministic and probabilistic approaches to simulate bifenthrin concentration in urban runoff
  Pair SWMM and VVWM
Identify sensitive input parameters with respect to model output

## Slide 2: Motivation / Background
Pyrethroids are often used by Professional Pest Control applicators and homeowners in residential settings
  California Department of Pesticide Regulation (CDPR) observed ≥ 1 pyrethroids in 78% of samples, 2009 – 2018
Identified as leading cause of invertebrate toxicity
  Pyrethroid detections often exceed US EPA aquatic life benchmarks
Impervious surfaces likely contribute to high observed concentrations
  No current models equipped for variability of urban environment

## Slide 3: SWMM
Storm Water Management Model (v. 5.1)
Simulates rainfall-runoff scenarios
  Runoff component
    Subcatchments receive precipitation and generate runoff and pollutant loads
  Routing component
    Transports runoff from each subcatchments through a series of conduits
Best suited for urban environment
Read SWMM Notes (Generic) and the SWMM User Manual for more in-depth discussion

## Slide 4: VVWM
Variable Volume Waterbody Model
Simulates water bodies receiving surface runoff
  Feed VVWM runoff and bifenthrin outputs from SWMM
Estimates fate and concentration for water column and benthic region

## Slide 5
Pleasant Grove Creek
Centered around Roseville, CA
Imagery shows residential, urban layout of our site

## Slide 6
Show the research flow diagram, and refer to GAME PLAN doc  has extensive notes on each aspect, as well as the manuscript methods

## Slide 7: Base SWMM model
Initial Setup
Created by Sumathy Sinnathamby
Raingages
1 daily precipitation file for entire watershed
Used data collected from HMS
Landuses
Developed (open, low, medium, high)
Other (all other landuses)
Buildup
External time series of application rates for Developed landuse
No buildup for Other landuse
Washoff
Exponential function for Developed landuse (coefficient = 1, exponent = 0.066)
No washoff for Other landuse
* Read GAME PLAN document for more detail

## Slide 8: SWMM to VVWM
SWMM outputs (runoff, bifenthrin) are fed into VVWM
SWMM outputs were forked into 7 VVWM runs
  Each of the 7 runs has its own receiving waterbody, which coincides with an observed storm drain outfall
  The SWMM outputs of the subcatchments whose runoff collects to that outfall are collated into VVWM inputs

## Slide 9: Folder Organization
The preceding slides discuss and explain the folder organization and the files within them.
I recommend going through the scripts in /probabilistic_python/src/ to get a better idea of the project flow and where the files are being incorporated, but these slides will help to provide additional information if you need it.

## Slide 10
/src/
  Scripts that create SWMM’s app rate time series file (01.R – 05.R)
  Scripts for assessing the apps input into SWMM vs. the apps that are present in SWMM output (compare.py, compare.R)
/output/
  Outputs created during the compare.R script processes
/io/
  Input and/or outputs created during the compare.R script processes
/figures/
  Figures created during the compare.R script processes
/calpip/
  contains the raw data downloaded from the CALPIP PUR database and subsequent files that were created in the data cleaning process
  File of importance: /app_rate_output_for_swmm_48rain.txt  the app time series file that is referenced in SWMM simulations

## Slide 11
This a just an active rough draft script that I use to test code before running in PyCharm.

## Slide 12
/analyze_pgc_sites.R
  Script that filtered the original observed data
  Also contains code to look a little at our specific outfalls of interest
/SURF_water.csv
  Original observed data
/SURF_water_placer_bifenthrin.csv
  Filtered product from the original (pesticide = bifenthrin & county = Placer )
  File of Importance
    You will use in the future to compare to modeled VVWM output. You will need to further divide this file by the ‘Site_code” to compare to model outputs

## Slide 13
Folder to contain final project outputs
Currently contains various presentations that were created during the project process…none are complete or presentation-worthy at this time

## Slide 14: Folder Organization
The preceding slides will discuss the /probabilistic_python/ folder in more detail

## Slide 15
Contains SWMM and VVWM executables, as well as their reference manuals
  Files of Importance (both are informative)
    /swmm_user_manual.pdf
    /VVWM_RevA.pdf

## Slide 16
This figure is just referenced in the SWMM input file
  Created by Sumathy Sinnathamby in the initial SWMM setup process

## Slide 17
/lhs_param_ranges.csv
  Pre-determined ranges when conducting LHS for SWMM variables
/lhs_param_ranges_vvsm.csv
  Pre-determined ranges when conducting LHS for VVWM variables

## Slide 18
Overall, this is the holding tank for the SWMM side of things. The necessary SWMM info from this folder gets transferred to the input/vvwm/ folder.
/input_/
  Folders of importance
  Folders that will be created and will contain SWMM files for nsims of the probabilistic process (have only run nsims=5 due to space restraints)
  The files within these folders do not reflect the most recent changes in the scripts
/NPlesantCreek.inp
  File of Importance
  SWMM input file
  Serves as the input file for the deterministic SWMM simulation, as well as the base file that the probabilistic simulations are built upon
/NPlesantCreek.out
  File of Importance
  SWMM binary output file
  Output is deciphered and read, and the necessary info is output into the .csv files (script 01b)
/NPlesantCreek.rpt
  Another SWMM output file; mainly a general overview of the simulation. We aren’t using this in the process.

## Slide 19
For each simulation, there is a single SWMM run. That SWMM run then gets forked into 7 VVWM runs (whose receiving waterbody coincides with an outfall (“Site_code”) in the observed dataset). The information pertaining to each of these VVWM runs are within their respective folder.
The next slide explains the content in the /outfall_31_26/ folder as an example

## Slide 20
/determ/ contains the VVWM simulation files for the deterministic approach
  vvwmTransfer.txt
    File of Importance
    VVWM variable info is contained here
  output.zts
    File of Importance
    SWMM outputs are converted to VVWM units and compiled into this file
  vvwm_wet.dvf
    File of Importance
    Weather file for VVWM
  output_.txt and output_.csv are created during the VVWM run
  runf_for_vvwm.csv and bif_for_vvwm.csv were created post-SWMM. They contained the converted values to be used in the output.zts file
/input_/ folders will contain all the necessary VVWM run files for that probabilistic simulation
  Folders of Importance
/outfall_31_26.csv provides a list of subcatchments that coincide with this outfall
  File of Importance
All other files contain compiled deterministic or probabilistic VVWM outputs, to be used later

## Slide 21
/lhs_sampled_params.csv
/lhs_sampled_params_vvwm.csv
  Files of Importance
  Both files contain the resulting variable values from the LHS. These values are used during the probabilistic process.

## Slide 22
Files of Importance
  File names should explain the main objective of the script.
  Script 11_ is incomplete.

## Slide 23
.csv files were downloaded from HMS to create the weather files
Scripts 01_ and 02_ create the weather files in their necessary format
swmm_wet.txt
  File of Importance
  SWMM weather file
vvwm_wet.dvf
  File of Importance
  VVWM weather file

## Slide 24: Contact Information
If you have any questions, please contact me at echelsvig@gmail.com